## Slide 1: The impact of non-maintenance of roads on freight to market Otto van Griethuysen 082 564 6842 1

## Slide 2: Main variables affected
Driver fatigue
Tyres
Chassis and cab
Maintenance
Fuel consumption
Trip time
These will be discussed using the Road Freight Association Vehicle Cost Index Edition 029 June 2024 as a base
All estimates are shown – per truck per annum

## Slide 3: Model used in the presentation

## Slide 4: Driver fatigue
Not easy to quantify but
Driver fatigue is a contributor to heavy vehicle incidents
Dodging potholes and bad pavement breakup increases the driver’s concentration and his fatigue level
This will also have an impact on Trip Times

## Slide 5: Tyre cost Badly maintained roads leads to premature tyre failure
Impact fractures
Sidewall damage
Both above leads to instant destruction of the tyre
Leads to less expected km per tyre
A standard Interlink with dropside body doing 140 000 km / annum
Depending on the frequency of using these roads
At 20% Premature failure = R72 800 Additional cost
At 40% Premature failure = R196 000 Additional cost

## Slide 7: Chassis and Cab
Not easily quantified - BUT
Cab rattling – This can also affect the driver’s concentration
Chassis and running gear damage
  Chassis cracks
  Under carriage damage
  Steering damage
This can lead to a very costly repair which cannot easily be quantified but it will lead to losses to the Transport company which he cannot recover from his customers

## Slide 8: Maintenance
The maintenance cost will also be higher on Under maintained roads
This is also not easy to quantify but a fair estimate would be an increase of 15% to 30% depending on the frequency of using these roads
A standard Interlink with dropside body doing 140 000 km / annum
Depending on the frequency of using these roads
At 15% increase = R26 250 Additional cost
At 30% increase = R52 500 Additional cost

## Slide 10: Fuel Consumption
For this variable I used Gauteng fuel price + 3 cents/liter
Another fuel grid will increase or decrease the additional cost
Due to the road conditions, there will be additional gear changes due to dodging bad patched slowing down and speeding up again
This will lead to an increase in fuel consumption
A standard Interlink with dropside body doing 140 000 km / annum
Depending on the frequency of using these roads
This can lead to an increase of 10% to as high as 20%
At 10% increase = R151 200 Additional cost
At 20% increase = R302 400 Additional cost

## Slide 12: Trip Times (1)
Due to the road conditions the trip times will also increase
Depending on the route and the frequency of using these roads the trip times can increase with 20% to 40% which in turn more trucks will have to be used to do the required work
A standard Interlink with dropside body doing 140 000 km / annum
Depending on the frequency of using these roads
At 20% increase in trip time (km per annum reduce to 112 000 km)
At 40% increase in trip time (km per annum reduce to 84 000 km)

## Slide 13: Trip Times (2)
This reduction in annual km will also increase the required R/km that the transporter needs to get to have a sustainable business
The trip time effect is shown in the next table
More vehicles / combinations will be required to take up the drop in productivity

## Slide 14: Combined Cost Increases
From the table we can see the impact of trucks using under maintained roads

## Slide 15: Closing Comment
The additional costs per vehicle per annum is high
Unfortunately, there is no exact data available - BUT
Imagine the total cost per annum if only 10% of the trucks use bad roads 20% of the time
This cost is carried by either the transporter and/or his customer

## Slide 16: Thank you Any questions ?